## Slide 1: Overhead Detail Inspection (ODI) Training
New Electrical System Inspectors (ESI)
Module 2: ODI Safety
Notes: The instructor notes for this course are divided into four sections, as is applicable:
References: Provides resource information about the source of the course content
Purpose: To explain the approach and intention of each slide
Delivery: To provide information and content to discuss with the group
  (Note: Some slides will not have specific delivery information. In this case, just present the contents of the slide.)
Checks: This section references the slide and uses as a type of asterisk. Its purpose is to remind the instructor to make the practical application of the course content to another program (e.g., Safety, Error Prevention, Rules That Will Keep You Alive, SCE Values & Goals, etc.)
------------------------------------------------
For this slide:
References:
Accident Prevention Manual (APM) Rules P15, 109, 111, 123, & 124
Distribution Inspection and Maintenance Program (DIMP) manual
ODI Tailboard Form for CMS
Purpose: ODI Safety
Delivery:
Module 2 duration: 30 minutes
Instructor-led training
Slide Usage Information
Slide time:
Purpose:

## Slide 2: Welcome & Introductions
Notes: Purpose: Introductions
Delivery:
Introduce yourself and ask the students to introduce themselves and their work location
NOTE: Slides 2-4 appear in all of the modules of this course in the event that multiple instructors teach and/or over multiple days. Feel free to skip these slides as necessary.

## Slide 3: Safety First!
First Aid kit
Volunteers
Earthquake procedures
In case of fire
Emergency exits
Where to gather outside
Notes: Purpose: Safety first
Delivery:
Review safety procedures
Understand what to do in an emergency

## Slide 4: Logistics & Guidelines
Cell phones/pagers off or silent
Restroom locations
Scheduled breaks and meals
Length of training
Class rules and guidelines
Notes: Purpose: Review class rules
Delivery: Review the classroom rules with students

## Slide 5: ODI Safety

## Slide 6: Learning Objectives
At the end of this module, students will be able to:
  Explain the requirements of ODI safety for ESIs
  Explain the requirements of and for the Self-Tailboard
  Discuss the guidelines for Personal Protective Equipment (PPE)
  Discuss the requirements of safe driving and parking
  Describe Environment, Health, & Safety (EHS) incidents
  NOTE: Please see the Accident Prevention Manual (APM) on the website
Notes: Reference: Accident Prevention Manual (APM)
Purpose: Understand the requirements of the module
Delivery: Review slide with students

## Slide 7: Module Overview
ODI Safety
Self-Tailboard
Personal Protective Equipment (PPE)
Driving and Parking Rules
Environment, Health, & Safety (EHS)
Notes: Purpose: Prepare students for module
Delivery:
Review a high-level overview of the module with students
NOTE: Information regarding dog safety is located in Module 10: Private Property
Slide Usage Information
Slide time:
Purpose:

## Slide 8: ODI Safety
Driving safely
Performing a self-tailboard when necessary
Wearing your Personal Protective Equipment (PPE) when in the field
Being aware of hazards to the public
Not placing yourself in “series” with ground-wire conductors
Notes: Purpose: Discuss ODI safety
Delivery: Discuss the notes below with students
Safety includes not only being aware of your surroundings and careful around electrical wires, it also includes:
Safe driving
Performing a self-tailboard when necessary
Always wearing your Personal Protective Equipment (PPE)
Being aware of hazards to the public
Be aware to not place yourself in “series” with ground-wire conductors as this may cause serious injury
For example: if the ground conductor is separated and you have one hand on one piece of the separated wire and the other hand on the other piece of separated wire, you have placed yourself in “series” possibly allowing voltage to flow through your body causing serious injury
Slide Usage Information
Slide time:
Purpose:

## Slide 9: ODI Safety (cont.)
S.T.O.P. Call for Assistance
Series Examples
S.T.O.P. Extremely Dangerous
Notes: Purpose: See examples
Delivery: Same as slide
Slide Usage Information
Slide time:
Purpose:

## Slide 10
If you have any questions regarding a potentially hazardous condition, call your Supervisor or Safety Specialist!!!
S.T.O.P.
Notes: Purpose: Discuss the S.T.O.P. process
Delivery: Same as slide
Slide Usage Information
Slide time:
Purpose:

## Slide 11: ODI Safety (cont.)
Ground Wire Conditions:
  Ground molding repairs
  Cover with 2” U-Groove
  Do not make repairs on broken ground wires. If the:
    Wire is broken and the ESI can safely cover it – cover it and create a P2 to repair the wire
    Wire is broken and the ESI cannot safely cover it – contact your supervisor and report a P1
Notes: Purpose: Discuss ODI safety
Delivery:
Do make the following repairs on poles:
Ground molding repairs
If the ground wire is broken, cover it and turn in a Priority 2 Repair Request with a short schedule date
Do not make repairs on broken ground wires
Slide Usage Information
Slide time:
Purpose:

## Slide 12: ODI Safety (cont.)
Notes: Purpose: Discuss ODI safety
Delivery: Same as slide
Slide Usage Information
Slide time:
Purpose:

## Slide 13: Self-Tailboard
You should always:
  Perform a self-tailboard
  Identify tasks and hazards
  Overcome hazards
  Repeat as necessary
ODI Self-Tailboard Checklist
Notes: Reference: ODI Self-Tailboard Checklist
Purpose: Same as slide
Delivery: An employee, working alone, shall perform a self-tailboard (Refer to the separate Daily Self-Tailboard Checklist)
Before starting every job, even if you are the only person doing the job
Ensure all tasks and hazards are identified
Overcome hazards prior to performing the task
Repeat as often as necessary to maintain safety
If there is a change during or after the job:
Contact your supervisor prior to beginning or continuing the work
Re-tailboard
Slide Usage Information
Slide time:
Purpose:

## Slide 14: ESI Self-Tailboard for iPad
Notes: Purpose: ESI Self-Tailboard for iPad
Delivery: Discuss with students

## Slide 15: Personal Protective Equipment (PPE)
Requirements:
  Wear a garment with full length sleeves, no short pants
  Wear approved head protection
  Wear suitable gloves with cuffs
  Wear approved warning vests
  Wear work shoes
  Wear safety glasses
Notes: References:
APM Rule 109 – Clothing
APM Rule 111 – Sight Protection
Purpose: Review required PPE
Delivery:
APM Rule 109 – Clothing:
Employees shall wear approved head protection (check inside hat for expiration date) when working:
  In locations where the hazards of flying or falling objects or substances are inherent in the work or environment
  On poles or structures
  In switch yards
Wear a garment with full length sleeves (rolled down) when working:
  On or with wood poles or crossarms
  In proximity to conductor
  Under other conditions as the supervisor directs
Wear suitable gloves with cuffs while working:
  On or with wood poles or crossarms
  Under other conditions as the supervisor in charge directs
Employees exposed to vehicular traffic shall wear approved warning vests marked with or made of high-visibility material
Employees shall wear work shoes only, no tennis shoes
APM Rule 111 – Sight Protection:
Approved eye-protection devices should fit properly, be kept clean at all times, shall not be altered, and shall be worn when an employee is engaged in or in the vicinity or work involving:
  Dust or flying particles
  Any other job where there is recognized danger of eye injury
NOTE: Face shields shall only be worn over, or in conjunction with, approved eye protection. Face shields are not approved eye protection.
Slide Usage Information
Slide time:
Purpose:

## Slide 16: PPE – AR/FR Clothing
Any hi-vis shirt in the company approved program…
Plus any pair of pants in the company approved program…
Or…
Benchmark and Tecgen coveralls can be worn alone
Notes: Reference: Arc Flash Compliance Training
Purpose: Review PPE
Delivery: Same as slide

## Slide 17: Care & Maintenance of PPE
Notes: Reference: Arc Flash Compliance Training
Purpose: Review care and maintenance of PPE
Delivery:
Refer to the Tyndale FRC Care, Maintenance, & You card included in your delivery
NOTE: SCE does not promote users to repair their own AR PPE. SCE has negotiated with Tyndale to perform minor repairs for end users. This helps maintain garment integrity.

## Slide 18: Driving
Knowledge and compliance with laws – APM P15
  State vehicle codes
  Local traffic rules
  Traffic control signs
  Posted speed limits
  Parking restrictions
  Company rules and regulations
Notes: Reference: APM P15
Purpose: Discuss driving requirements
Delivery: Drivers of vehicles shall be familiar with and obey:
All State Vehicle Codes
Local traffic rules and ordinances
Traffic control signs
Posted speed limits
Parking restrictions
All Company rules and regulations governing vehicle operation

## Slide 19: Driving (cont.)
License Requirements – APM P15
  Valid driver’s license
  Driver’s license status
  Defective vehicle
  Portable electronic devices
Parking – APM Rule 123
  Sharp tools
  Secured loads and riders
  Rider must be seated
  Restraint devices
Notes: References: APM Rules P15 & 123
Purpose: Discuss driving requirements
Delivery:
Drivers of vehicles shall have in their possession at all times a valid driver’s license appropriate for the type of equipment to be operated. Any change in the status of an employee’s drivers license shall be reported immediately to his/her supervisor.
Drivers shall not operate vehicles with faulty brakes or mechanical defects such as faulty steering mechanism or lights, except to proceed to a place where repairs can be made, and then only at such reduced speed or in such a manner that will enable the movement to be made safely. Such conditions shall be reported in writing in accordance with existing instructions.
Employee use of all company-provided, hand-held, portable electronic devices is prohibited while driving
Personal hand-held portable electronic devices are prohibited while driving on company business, on company property, and in company vehicles
Any other distractions apply as well
Exceptions: Where it is legally permitted, the following exceptions apply:
  Hands-free equipment
  800/900 MGHz radios
Prohibited use of hand-held electronic devices includes the following:
  Talking
  Dialing
  Checking voicemail messages
  Entering data or reading text
Prohibited hand-held electronic devices include:
  Cell phones
  Blackberrys
  Pagers
  Personal Digital Assistants (PDAs)
  Portable Global Positioning Systems (GPS)
  Meter reading hand-held devices
  Other portable electronic communication devices
Turn off cell phone or handset before entering vehicle
Even with hands-free equipment, never take a call if it is not safe
If using hands-free equipment and if it is safe:
  Pull over to the side of the road before answering call
  Answer call and ask if you can call back when you arrive at destination
Slide Usage Information
Slide time:
Purpose:

## Slide 20: Driving (cont.)
Parking – APM Rule 124
  Parking regulations
  Construction signs and cones
  Safe parking
Notes: Reference: APM Rule 124
Purpose: Discuss driving requirements
Delivery:
Drivers shall comply with state and local parking regulations except when exemption is granted for work involving construction, operation, removal, or repair of utility facilities
Vehicles parked under the foregoing special conditions must be protected by specified warning devices (Construction signs and cones)
When any motor vehicle is parked on a grade, the operator shall turn the front wheel against the curb, set the emergency brake, and place the transmission in gear or parking position
Slide Usage Information
Slide time:
Purpose:

## Slide 21: Environment, Health, & Safety (EHS)
Examples:
  Leaving the engine idling for long periods of time (i.e., environment concern)
  Parking a hot truck on dead, long grass (i.e., environment and safety concerns)
Potential risks:
  Oil release
  Oil leak
  Oil spill
Notes: Purpose: Discuss the environmental concerns regarding idling for long periods
Delivery:
Examples:
  Leaving the engine idling for long periods of time (environment)
  Parking a hot truck on dead, long grass (environment/safety)
Leaky transformer criteria:
  Oil visible or ½ way down the can – report as a P2
  Oil down to the bottom of the can/or in environment – report as a P1 and call the supervisor
Definitions:
  Oil Release – Oil in the environment, usually on the side of a piece of equipment
  Oil Leak – Oil release indicating evidence that the oil is fresh (and possibly moving) and the potential to contaminate the environment exists
  Oil Spill – Oil has spread to the environment
What to do:
  If the Priority 1 condition is due to an active oil spill, use an oil spill kit to contain the spread of oil
  The ESI reports the Priority 1 condition to their supervisor
  The supervisor contacts and reports the condition to the environmental specialist
Refer to the Notifications training module for complete information on reporting a Priority 1 condition
Slide Usage Information
Slide time:
Purpose:

## Slide 22: Module Wrap Up
Explain the requirements of ODI safety for ESIs
Explain the requirements of and for the Self-Tailboard
Discuss the guidelines for Personal Protective Equipment (PPE)
Discuss the requirements of safe driving and parking
Describe Environment, Health, & Safety (EHS) incidents
Notes: References:
Accident Prevention Manual (APM) Rules P15, 109, 111, 123, & 124
Distribution Inspection and Maintenance Program (DIMP) manual
ODI Tailboard Form for CMS
Purpose: Module wrap up
Delivery:
Discuss what was covered during the module
Emphasize critical points and mistakes/issues commonly made in the field
Ask for follow up questions

## Slide 23: Check Your Knowledge
Explain what a self-tailboard is.
Name 6 PPE items.
What is prohibited in the company distracted-driving policy?
What actions should an ESI take when he discovers oil on a transformer?
Notes: Instructor Notes
Explain what is a self-tailboard and when is it used?
Used as follows:
    Before starting the job
    During or after the job
    When there is a change
    As often as necessary to maintain safety
    A self-tailboard is:
    A checklist used to verify that you have all the items and equipment needed in your vehicle before you start inspections.
Name six PPE items.
    Hard Hat
    Safety Glasses
    Long Sleeve Shirt
    Warning Vest
    Gloves
    Boots
What usage is prohibited in the company distracted driving policy for hand-held electronic devices?
  Prohibited use of hand-held electronic devices includes the following:
    Talking
    Dialing
    Checking voicemail messages
    Entering data or reading text
What does an ESI do about oil spills?
If oil has spread to the environment:
    If the Priority 1 condition is due to an active oil spill, use an oil spill kit and contain the spread of oil.
    Report the Priority 1 condition as required and contact the environmental specialist.
Slide Usage Information
Slide time:
Purpose:
Purpose: Knowledge check
Delivery: Facilitate a discussion regarding what the answers to these questions are and why
Answers:
A safety check list that ESIs review prior to starting work that reminds them of unsafe hazards with rules and tips to keep them safe
Hard hat, leather gloves, safety glasses, approved long sleeve shirt, and shoes
Portable electronic devices
Oil visible or ½ way down the can – report as a P2
Oil down to the bottom of the can/or in environment – call the supervisor to report as a P1

## Slide 24: End of ODI Safety Module