## Slide 1: Overhead Detail Inspection (ODI) Training
New Electrical System Inspectors (ESI)
Module 10: Private Property
Notes: The instructor notes for this course are divided into four sections, as is applicable:
References: Provides resource information about the source of the course content
Purpose: To explain the approach and intention of each slide
Delivery: To provide information and content to discuss with the group
  (Note: Some slides will not have specific delivery information. In this case, just present the contents of the slide.)
Checks: This section references the slide and uses as a type of asterisk. Its purpose is to remind the instructor to make the practical application of the course content to another program (e.g., Safety, Error Prevention, Rules That Will Keep You Alive, SCE Values & Goals, etc.)
------------------------------------------------
For this slide:
Purpose: Inspections on private property (formerly called “Backyard Inspections”)
Delivery:
Module 2 duration: 45 minutes
Instructor-led training
Slide Usage Information
Slide time:
Purpose:

## Slide 2: Welcome & Introductions
Notes: Purpose: Introductions
Delivery:
Introduce yourself and ask the students to introduce themselves and their work location
NOTE: Slides 2-4 appear in all of the modules of this course in the event that multiple instructors teach and/or over multiple days. Feel free to skip these slides as necessary.

## Slide 3: Safety First!
First Aid kit
Volunteers
Earthquake procedures
In case of fire
Emergency exits
Where to gather outside
Notes: Purpose: Safety first
Delivery:
Review safety procedures
Understand what to do in an emergency

## Slide 4: Logistics & Guidelines
Cell phones/pagers off or silent
Restroom locations
Scheduled breaks and meals
Length of training
Class rules and guidelines
Notes: Purpose: Review class rules
Delivery: Review the classroom rules with students

## Slide 5: Private Property

## Slide 6: Learning Objectives
At the end of this module, students will be able to:
  Outline the responsibilities of the ESI for performing ODIs on private property
  Explain that safety is the first responsibility of each SCE employee, that ESIs must be aware of their surroundings
  Detail the proper actions to stay safe in potentially unsafe conditions
  Discuss the entry and exit guidelines for performing ODIs on private property
  Describe access issues an ESI faces and how to approach or remedy them
Notes: Purpose: Understand the requirements of the module
Delivery: Review slide with students
Slide Usage Information
Slide time:
Purpose:

## Slide 7: Module Overview
Responsibilities
Inspection Safety
Prior to Entry
Entry Guidelines
Access Exceptions
Pole Access
Inspection
Exit Guidelines
Notification
Notes: Purpose: Prepare students for module
Delivery: Review a high-level overview of the module with students
Slide Usage Information
Slide time:
Purpose:

## Slide 8: Responsibilities
Residential
Commercial
Agricultural
Notes: Purpose: Discuss responsibilities when working on private property
Delivery: The Private Property procedures assist in providing safe entry into backyards for pole inspection on private properties including:
Residential
Commercial
Agricultural
Slide Usage Information
Slide time:
Purpose:

## Slide 9: Responsibilities (cont.)
ODI Supervisors
ESIs
Notes: Purpose: Discuss responsibilities
Delivery: Review the responsibilities of supervisors and ESIs
Supervisors – Train, implement, and ensure that all ESIs in their group adhere to ODI procedures
ESIs – Comply with the ODI procedures and incorporate them into their daily inspections
Slide Usage Information
Slide time:
Purpose:

## Slide 10: Responsibilities (cont.)
Safety
Quality
Productivity
Notes: Purpose: Discuss responsibilities
Delivery: Review the responsibilities regarding the following items:
Safety – ESIs must be aware of their surroundings at all times and take the necessary action to remove themselves from an unsafe environment
Quality – ESIs must meet the minimum standard quality requirement of 94% for Priority 1 and 2 findings and 92% for Priority 3 findings
Productivity – ESIs must be able to inspect and repair a minimum of 55 poles per day
Slide Usage Information
Slide time:
Purpose:

## Slide 11: Inspection Safety
Right to access
Perform inspection
Notes: Purpose: Discuss responsibilities regarding inspection safety
Delivery:
Edison employees have the right to access SCE equipment for maintenance and inspection
ESIs are expected to enter areas where SCE distribution poles exist to perform inspection and public level repairs
Slide Usage Information
Slide time:
Purpose:

## Slide 12: Inspection Safety (cont.)
Feel unsafe driving
Repair feels dangerous
Condition might cause strain
Access compromises safety
Avoid unstable surfaces
Avoid lifting heavy or awkward objects
Avoid unsafe areas
Use extra caution
Notes: Purpose: Discuss responsibilities regarding inspection safety
Delivery:
Employees working in the field may be exposed to unsafe conditions – Each ESI is responsible to avoid any unsafe condition
For example:
  If you feel unsafe driving, slow down, pull over, or stop to return to a safe condition
  If a repair feels dangerous, notify your supervisor instead of doing the repair
  If a condition might cause strain (e.g., reaching, lifting, or bending), do not perform the task
If gaining access to a structure may compromise safety (e.g., climbing, heavy vegetation, leaving cell phone or contact range, or entering a bad neighborhood), stop and notify your supervisor
  Avoid unstable surfaces
  Avoid lifting heavy or awkward objects
  Avoid unsafe areas when evaluating access
  Use extra caution in deteriorated driving conditions (e.g., rain, ice, fog, high winds, etc.)
Slide Usage Information
Slide time:
Purpose:

## Slide 13: Inspection Safety (cont.)
Properties have risks
Be aware of surroundings
Remove yourself from an unsafe environment
Safety is the first responsibility
Inspect the pole from a distance
If a hazard exists, contact your supervisor
Notes: Purpose: Discuss responsibilities regarding inspection safety
Delivery:
Inspectors must always be aware of their surroundings because backyards and private properties have inherent risks. If you feel that you are in a unsafe environment, immediately remove yourself from it. Remember that safety is the first responsibility of each SCE employee.
Before approaching a structure, inspect the pole from a distance for potential Priority 1 safety hazards. If a hazard exists, contact your supervisor and report the condition using ODI-05, “Reporting Priority 1 Conditions.”
Slide Usage Information
Slide time:
Purpose:

## Slide 14: Prior to Entry
Determine the exact location of the pole
Verify or enter property address
Inspect structure without entering area
Create “Obstruction Exception,” if necessary
Not always necessary to notify customer
Notes: Purpose: Discuss responsibilities regarding entry
Delivery:
Determine the exact location of the pole for inspection. Sometimes a pole may appear to be in one backyard, but may instead be in an alley or in another backyard.
When the location is determined, verify or enter the correct property address for the pole
Determine if the structure can be inspected without entering the area
If there are obstacles that cause limited inspection, entry may not be necessary
If the pole and Edison equipment cannot be seen, create an “Obstruction Exception”
In commercial and agricultural areas, it is not always necessary to notify customers prior to entry
Slide Usage Information
Slide time:
Purpose:

## Slide 15: Prior to Entry (cont.)
Attempt to notify customer
If the customer is not home
If it is not safe: Do Not Enter
Notify your supervisor
When safe, enter yard
Dog Bite Prevention (click to view)
Notes: Purpose: Discuss responsibilities regarding entry (continued)
Delivery:
For residential and commercial properties, when access is necessary, approach the front door and attempt to notify the customer that access to the SCE structure is necessary for inspection and ask the following:
  Is there any reason their yard is unsafe for entry?
  Do they have pets that have yard access?
If an adult customer is not home, determine if conditions are safe and look for the following:
  Signs of dogs or dangerous pets (CLICK LINK TO SHOW VIDEO = approximately 14 minutes)
  Illegal activity
  Gate or other safe path for entrance
  Vehicular traffic and operating machinery
  Hazardous clutter and obstructions
  Farm or ranch animals
  Fresh insecticides
If conditions are not safe: do not enter
If conditions can be made safe with the help of a second ESI, make a note, and notify your supervisor
When conditions are safe, enter the yard

## Slide 16: Entry Guidelines
Right to access SCE equipment
Try access point
  Do not walk through residence
  Do not use ladders
Use caution
  Enter yard if safe
  Take safety equipment
  Evaluate path
  Move items
  Go directly to pole
Notes: Purpose: Discuss responsibilities regarding entry guidelines
Delivery:
SCE employees have the right to access SCE equipment for maintenance and inspection purposes
After access is granted, the ESI should try to access through a yard gate, garage, or other access point
  Do not walk through a residence unless that is the only access to the structure
  Do not use ladders to gain access
Consider the following and use extra caution when entering and exiting private property:
  Only enter the yard after determining if it is safe to do so
  Take needed safety equipment into the yard
  Evaluate the path to the pole
  Move items when necessary to gain access
  Go directly to the pole and move around the yard to view all SCE equipment as required
Slide Usage Information
Slide time:
Purpose:

## Slide 17: Entry Guidelines (cont.)
Be careful not to:
  Bump into equipment
  Contact machinery
  Track debris
  Leave items
  Linger
Notes: Purpose: Discuss responsibilities regarding entry guidelines
Delivery: Be careful not to:
Bump into equipment or materials on customer’s property
Make contact with machinery on private property
Track debris in and out of the area
Drop or leave items behind or in the pathway
Linger
Slide Usage Information
Slide time:
Purpose:

## Slide 18: Access Exception – Entry Access
If adequate access is not possible, enter a note for “Limited Inspection”
Make a second entry attempt later if possible
If no access on the second attempt, hang another door hanger and enter this action in the field tool
After the second attempt is unsuccessful, create a “No Access” exception
Notes: Purpose: Discuss responsibilities regarding access
Delivery:
There are two types of access exceptions. The first of which is entry access.
  Entry Access – refers to whether or not the inspector can gain entry into the yard. If the limitation is access, inspect the pole, enter “Limited Inspection,” and select “Access” as the reason. Also, enter comments and a picture to describe the access limitation.
If the ESI does not have adequate access to view and determine the safety and reliability of Edison equipment, enter a note that they were unable to gain access and will return to gain access when the customer is home
When possible, make a second entry attempt to inspect the pole at either the beginning or end of the day
If no access is obtained on the second attempt, hang another door hanger and enter this action in the field tool
After the second attempt is unsuccessful, and before the work order is closed, create a “No Access” exception
Slide Usage Information
Slide time:
Purpose:

## Slide 19: Access Exception – Obstruction Access
Large amount of debris
Piles of wood
Excessive vegetation
Items permanently fixed to the pole
Heavy equipment
Permanent irrigation
Notes: Purpose: Discuss responsibilities regarding access
Delivery:
The second type of access exception is obstruction access:
  Obstruction Access – refers to whether or not the path to the structure or the structure itself is obstructed. The structure may be inaccessible if it is obstructed by vegetation or objects. If the limitation is obstruction, inspect the pole, enter “Limited Inspection,” and select “Obstruction” as the reason. Also, enter comments and a picture to describe the access limitation.
Determine if an obstruction can be safely moved. If it is excessive, do not attempt the move.
Call for the assistance of another inspector. For example, do not move:
  Large amount of debris
  Piles of wood, boards, or other construction material
  Excessive vegetation such as bushes, tall plants, and trees growing around the pole
  Items permanently fixed to the pole such as fences, gates, and chained items
  Heavy equipment such as boats, cars, trailers, etc.
  Permanent irrigation such as PVC lines
Slide Usage Information
Slide time:
Purpose:

## Slide 20: Access Exception – Obstruction Access (cont.)
Move obstructions to safe place
Return items to original location
Lift only what you feel safe moving
Limit effort to not apply force
Manipulate heavy objects
Notes: Purpose: Discuss responsibilities regarding access
Delivery:
Non-vegetation path obstructions that must be moved shall be moved into a safe location
For example:
  If you move a bicycle, place it in a location where it will be safe for people and vehicles and will not fall over and cause damage to itself or another item
  Return moved items to their original location unless it would cause an unsafe condition
CAUTION:
  An ESI shall not lift more weight than they feel safe moving with a limitation not to exceed 50 pounds
  Inspectors shall limit their effort to avoid using force that may cause strain or injury
  You can move an object that is heavier than 50 pounds (e.g., rolling a trash can, etc.)
Slide Usage Information
Slide time:
Purpose:

## Slide 21: Pole Access
Make reasonable effort to gain access to pole
  Use sound judgment
  Move brush
  Avoid dangerous vegetation
Determine accessibility
  Use stick to identify holes
  Determine if safe to ascend hill
  Only climb hillsides
  Step on secure footing
  Get assistance from another ESI
Notes: Purpose: Discuss responsibilities regarding access
Delivery:
Make a reasonable effort to gain access to the pole and use sound judgment when accessing poles
  When necessary, the ESI can walk in flower beds, step into ground-level brush, and move brush or small limbs (if possible) to get to the structure
  ESIs shall not come in contact with thorny vegetation such as bougainvillea or rose bushes, and avoid poison ivy, oak, and sumac
Use good judgment when determining if they should access a pole. For example:
  If needed, use a stick to probe ground level bushes or shrubs to identify holes or other safety concerns
  Use sound judgment when determining if it is safe to ascend a hill
  Generally, do not climb on anything other than hillsides
  Do not step on anything without secure footing
  The ESI may need to get assistance from another ESI to complete an inspection
Slide Usage Information
Slide time:
Purpose:

## Slide 22: Inspection
Perform public repairs
Correct conditions
Notes: Purpose: Discuss responsibilities regarding safe inspections
Delivery:
Complete a detailed inspection and perform public repairs at that location when safe to do so
It is not acceptable to leave a condition that can be corrected and then create a notification to call out another crew to perform these functions
CAUTION: At no time shall ESIs put themselves at potential risk of personal injury, equipment damage, or property damage
Slide Usage Information
Slide time:
Purpose:

## Slide 23: Inspection (cont.)
Make public level repairs
Trim vegetation to make repair
Notes: Purpose: Discuss responsibilities regarding safe inspections
Delivery: For Public Level Repairs:
Inspectors shall make a reasonable and safe effort to make public level repairs while at the pole
When necessary, an ESI should only trim enough vegetation so that he can make the repair
Do not remove very large amounts of vegetation (e.g., if there is ivy on the pole, only remove enough ivy to make a proper repair)
Slide Usage Information
Slide time:
Purpose:

## Slide 24: Exit Guidelines
Leave property as found
For maintenance inform customer
Place vegetation in container
Remove all tools
Close gates and doors
Notes: Purpose: Discuss responsibilities regarding exiting
Delivery: Be sure to leave the property in the same condition as it was found
If maintenance is scheduled, attempt to inform the customer
Place trimmed vegetation in a container (trash bag) and remove it from the yard
Remove all tools
Restore access as found; close gates and doors
Slide Usage Information
Slide time:
Purpose:

## Slide 25: Notification
Communicate concerns and infractions
Unauthorized attachments
Do not use for excessive vegetation
Notes: Purpose: Discuss responsibilities regarding notifications
Delivery:
Use the Third-Party Notification process for:
  Communicating safety and reliability concerns and G.O. infractions
  Customer notifications regarding unauthorized attachments to the pole
  If a public level infraction is identified, but the obstruction prevents the inspector from making a repair, create a Priority 2 or Priority 3 work notification
Do not use the Third-Party Notification process for excessive vegetation
Slide Usage Information
Slide time:
Purpose:

## Slide 26: Module Wrap Up
Outline the responsibilities of the ESI for performing ODIs on private property
Explain that safety is the first responsibility of each SCE employee, that ESIs must be aware of their surroundings
Detail the proper actions to stay safe in potentially unsafe conditions
Discuss the entry and exit guidelines for performing ODIs on private property
Describe access issues an ESI faces and how to approach or remedy them
Notes: Purpose: Module wrap up
Delivery:
Discuss what was covered during the module
Emphasize critical points and mistakes/issues commonly made in the field
Ask for follow up questions

## Slide 27: Check Your Knowledge
What are the 3 performance priorities for an ESI?
Name at least 4 potentially dangerous things to look for before accessing a property.
Name at least 3 types of obstructions that must not be moved by the ESI.
Why do you use the Third-Party Notification process?
How should you leave the property you inspected?
Notes: Instructor Notes
Answers
What are the ESIs three performance priorities?
  Safety
  Quality
  Productivity
Name at least four potentially dangerous things to look for before accessing a property.
  Signs of dogs or dangerous pets
  Illegal activity
  Vehicular traffic and operating machinery
  Hazardous clutter and obstructions
  Farm or ranch animals
  Fresh insecticides
Name several types of obstructions which cannot be moved by the ESI.
  Large amount of debris
  Piles of wood, boards or other construction material
  Excessive vegetation such as bushes, tall plants and trees growing around the pole
  Items permanently fixed to the pole such as fences, gates, and chained items
  Heavy equipment such as boats cars, trailers, etc.
  Permanent irrigation such as PVC lines
Use the Third-Party Notification process for:
  Communicating safety and reliability concerns
  Customer notifications regarding unauthorized attachments to the pole
  If a public level infraction is identified, but the obstruction prevents the inspector from making a repair, create a Priority 2 or Priority 3 work notification.
How do you want to leave the property you inspected?
Be sure to leave the property in the condition you found it.
Slide Usage Information
Slide time:
Purpose:
Purpose: Knowledge check
Delivery: Facilitate a discussion regarding what the answers to these questions are and why
Answers:
Safety
Quality
Productivity
Signs of dogs or dangerous pets
Illegal activity
Gate or other safe path for entrance
Vehicular traffic and operating machinery
Hazardous clutter and obstructions
Farm or ranch animals
Fresh insecticides
Large amount of debris
Piles of wood
Excessive vegetation
Items permanently fixed to the pole
Heavy equipment
Permanent irrigation
Communicating safety and reliability concerns and G.O. infractions
Customer notifications regarding unauthorized attachments to the pole
If a public level infraction is identified, but the obstruction prevents the inspector from making a repair, create a Priority 2 or Priority 3 work notification
Leave the property as you found it

## Slide 28: Private Property