## Slide 1: Overhead Detail Inspection (ODI) Training
New Electrical System Inspectors (ESI)
Module 9: Repairs
Notes: The instructor notes for this course are divided into four sections, as is applicable:
References: Provides resource information about the source of the course content
Purpose: To explain the approach and intention of each slide
Delivery: To provide information and content to discuss with the group
  (Note: Some slides will not have specific delivery information. In this case, just present the contents of the slide.)
Checks: This section references the slide and uses as a type of asterisk. Its purpose is to remind the instructor to make the practical application of the course content to another program (e.g., Safety, Error Prevention, Rules That Will Keep You Alive, SCE Values & Goals, etc.)
------------------------------------------------
For this slide:
Purpose: ODI repairs
Delivery:
Module 9 duration: 30 minutes
Instructor-led training
Slide Usage Information
Slide time:
Purpose:

## Slide 2: Welcome & Introductions
Notes: Purpose: Introductions
Delivery:
Introduce yourself and ask the students to introduce themselves and their work location
NOTE: Slides 2-4 appear in all of the modules of this course in the event that multiple instructors teach and/or over multiple days. Feel free to skip these slides as necessary.

## Slide 3: Safety First!
First Aid kit
Volunteers
Earthquake procedures
In case of fire
Emergency exits
Where to gather outside
Notes: Purpose: Safety first
Delivery:
Review safety procedures
Understand what to do in an emergency

## Slide 4: Logistics & Guidelines
Cell phones/pagers off or silent
Restroom locations
Scheduled breaks and meals
Length of training
Class rules and guidelines
Notes: Purpose: Review class rules
Delivery: Review the classroom rules with students

## Slide 5: Repairs

## Slide 6: Learning Objectives
At the end of this module, students will be able to:
  Discuss the precautions they must take prior to making repairs
  Describe the public level repairs they are expected to make
  Explain the proper actions to take for repairs they cannot make
Notes: Slide Usage Information
Slide time:
Purpose: Objective of this training module.
Purpose: Understand the requirements of the module
Delivery: Review slide with students

## Slide 7: Module Overview
Precautions
Public level repairs
Repairs to not make
Notes: Slide Usage Information
Slide time:
Purpose: Lists repairs for public level repairs on poles.
Reference: Accident Prevention Manual (APM) 204
Purpose: Prepare students for module
Delivery: Review a high-level overview of the module with students
SCE’s APM contains policies and safety rules for common work activities – Please read this manual and familiarize yourself with the policies and applicable safety rules
Testing Lines and Equipment APM 204:
  Before starting any repair work, be aware that electrical equipment and lines shall always be considered to be energized unless you are positive that they are de-energized
  Before starting work, a preliminary inspection shall be made to determine what conditions exist. Wires designed to operate at ground potential may sometimes become energized by reason of faulty or inadequate connections. Care shall always be exercised to handle ground wires with the same caution as is used with energized wires.
The pole’s public level section of the pole is from the ground up to as high as the ESI is able to reach
  This is the section of the pole where the ESI makes repairs
  Items to be repaired are in the following slides
Maintenance tasks not completed by an inspector will be assigned to Distribution construction and maintenance crews

## Slide 8: Public Level Repairs
Risers
  Make minor repairs on risers
  Cover damaged risers
Inspect poles
  Install pole number tags
  Install or replace visibility strips
  Repair or replace guy guards
Inspect area around poles
  Remove unauthorized attachments
  Remove minor obstructions
  Minor housecleaning
Notes: Slide Usage Information
Slide time:
Purpose: Objective of this training module.
Purpose: Discuss public level repairs
Delivery: The repairs described in this module of the ODI New ESI Training include the following:
Risers:
  Make minor repairs on risers
  Cover damaged risers
Inspect poles:
  Install pole number tags
  Install or replace visibility strips
  Repair or replace guy guards
Inspect area around pole:
  Remove unauthorized attachments
  Remove minor obstructions
  Minor housecleaning

## Slide 9: Public Level Repairs (cont.)
Repair or cover ground molding
  Ground wire is separated
  Ground wire is not separated
Notes: Purpose: Discuss public level repairs
Delivery: The repairs described in this module of the ODI New ESI Training include the following (continued):
Repair or cover ground molding:
  If the ground wire is separated:
    Cover with 2” U-Guard
    Turn in a repair request
  If the ground wire is not separated:
    Use an 8’ length of U-Guard for repairs
    Use lag screws to ensure they are solidly attached
    Be sure to secure tightly so no light can be seen between the pole and the molding

## Slide 10: Public Level Repairs (cont.)
Do not perform the following repairs:
  Splice broken ground wires
  Ground clamps (Acorns)
Notes: Slide Usage Information
Slide time:
Purpose: Do not make these repairs.
Purpose: Discuss public level repairs
Delivery: Do not do the following repairs on poles:
Do not splice broken ground wires.
  Be aware of hazards to the public
  Create a work request for repair
Do not attempt to repair ground clamps (e.g., “Acorns”)

## Slide 11: Public Level Repairs (cont.)
Notes: Slide Usage Information
Slide time:
Purpose: Grounding picture
Purpose: Discuss public level repairs
Delivery: Review diagram

## Slide 12: When Repairs Are Not Made
Overhead maintenance
  Assigned work order numbers
  Scheduled for completion
Repair Request
Notes: Slide Usage Information
Slide time:
Purpose: Work orders
Purpose: Discuss when repairs are not made
Delivery:
Maintenance tasks not completed by an inspector:
  Assigned work order numbers
  Scheduled for completion
Work orders are then assigned to distribution construction and maintenance crews

## Slide 13: Module Wrap Up
Discuss the precautions inspectors must take prior to making repairs
Describe the public level repairs inspectors are expected to make
Explain the proper actions to take for repairs inspectors cannot make
Notes: Purpose: Module wrap up
Delivery:
Discuss what was covered during the module
Emphasize critical points and mistakes/issues commonly made in the field
Ask for follow up questions

## Slide 14: Check Your Knowledge
What is the learning objective for this training module?
On a pole that an ESI is expected to make repairs on, what is the name of the level, where is it located?
Name three repairs that an ESI is expected to make.
Name two repairs that an ESI is not expected to make.
Notes: What is the learning objective for this training module?
    Learn what type of repairs need to be made,
    what repairs you are expected to make and
    how to make each repair.
What is the name of the level and where is it located on the pole at which an ESI is expected to make repairs?
    Public Level
    Located from ground level and as high as the ESI can reach
Name three repairs that an ESI is expected to make.
    Cover Damaged Ground Molding and Wires – Use 2” U-Grove to cover the wires and attach securely with lag screws.
    Cover Damaged Risers – Use 5” U-Groove to cover the riser and attach securely with lag screws.
    Install Pole Numbers – Validate the correct pole number in the FIM and that the new pole number tag is the correct pole number.
    Install or Replace Visibility Strips – Place strips at 3, 4, and 5 foot levels facing traffic. In a parking lot, wrap all the way around the pole.
    Repair or Replace Guy Guards – Repair or replace as needed.
Name two repairs that an ESI is not expected to make.
    Do not make repairs on broken Ground-Wire Conductors Turn in a Repair Request immediately and be aware of hazards to the public.
    Do not attempt to repair Ground Clamps (i.e. “Acorns”)
Student Notes
Slide Usage Information
Slide time:
Purpose:
Instructor Notes
Purpose: Knowledge check
Delivery: Facilitate a discussion regarding what the answers to these questions are and why
Answers:
What type of repairs need to be made
What repairs you are expected to make
How to make each repair
Public Level
Possible answers: Ground molding, replace guy guard, install pole tag, install visibility strips, repair riser, remove low pole steps, and remove unauthorized attachment
Repair broken ground wire
Repair ground rod clamps (Acorns)

## Slide 15: End of Repairs Module