## Slide 1: Trim RX Assessment

## Slide 2: Summary
Goal
Establish the evaluation methodology for the clearance-based trim RX algorithm
Context
The clearance-based trim RX algorithm has the following characteristics:
Inputs
  Classified remote sensing data
  Crown polygons
  Circuit vector models
Outputs
  Grow-in clearance distance and worst offending point for each crown polygon
  Fall-in clearance distance and worst offending point for each crown polygon
Recommendation
The clearance-based trim RX model should be assessed via desktop inspections
Assess approximately ~3000 geospatial tiles for assessment

## Slide 3: Potential Evaluation Methodologies
Field inspections
Desktop inspections
Clearance report comparison
Strategy
Send inspectors into the field to verify algorithm distances
Pros
Not reliant on remote sensing data
Cons
Difficult for inspectors to assess sag and sway
Potentially unreliable and impractical to assess reliability
Expensive, hard to scale
Strategy
Inspectors use QC tool to verify algorithm distances
Pros
Allows inspectors to see sag and sway conditions
Allows for assessment of remote sensing data
Creates dataset for future algorithm improvement
Reliability can be assessed via meta studies
Less expensive, easier to scale
Cons
Reliant on remote sensing data
Strategy
Assess clearance engine via running on LiDAR encroachment points and comparing with clearance reports.
Pros
Can be run at scale
Highly reliable
Inexpensive
Cons
Partial assessment of algorithm
  Only assesses clearance engine
Reliant on remote sensing data and clearance reports

## Slide 4: Sampling Strategy
Tile the relevant buffer of each circuit in sample
Take a stratified sample of the tiles, using the following strata
  Landcover (~5 classes)
  Circuit type (2 classes)
  Fire risk (2 classes)
Randomly sample at most one tree from each tile.
  Samples with no trees are not discarded so that reviewers can check that the algorithm did not miss trees.
First pass example
Population of 100 m^2 tiles: ~700K
  Generated from 4580 circuits in dev environment
Stratified sample of ~3000 tiles
  Results in at least 25 tiles in each strata combination
Sample geospatial tiles to assess the expected performance in any part of SCE’s service area.

## Slide 5: Metrics
The scoring function is defined for a crown as
The metric is aggregated over a collection of crowns as