## Slide 1
www.technosylva.com
www.wildfireanalyst.com
Updated: September 2nd, 2021
SCE PSPS threshold analysis
DRAFT version

## Slide 2
CONFIDENTIAL AND PROPRIETARY INFORMATION INCLUDED
The information provided in this file contains confidential and proprietary information regarding Technosylva’s Wildfire Analyst™ Enterprise modeling methods and algorithms. This information may not be shared in any form outside of the organization without the express written consent of Technosylva.
By accepting and opening this file understands and agrees to non-disclosure of this confidential information.
www.technosylva.com
Copyright © 2021. Technosylva Inc., La Jolla, CA.

## Slide 3
Table of Contents
STEP 1
PSPS Days – All Circuits in PSPS Days
  All circuits
  De-energized circuits in PSPS events
STEP2
Non-PSPS Days – circuits, thresholds. Fire season
www.technosylva.com
Copyright © 2021. Technosylva Inc., La Jolla, CA.
Table of Contents

## Slide 4
PSPS days
We extracted all circuit records for PSPS days (n = 220,688)
  Remove de-energized records (those records in PSPS days from de-energized circuits)
  Each circuit has fire risk metrics every 3 hours
  We filtered data using the thresholds previously calculated
    (Buildings OR Fatalities) and FBI (for each percentile threshold)
    Circuits that met the threshold criteria
PSPS Days – All Circuits in PSPS Days
www.technosylva.com
Copyright © 2021. Technosylva Inc., La Jolla, CA.
Percentile | Buildings | Fatalities | FBI
50th | 182 | 0.22 | >=4
75th | 455 | 0.51 | >=4
80th | 535 | 0.57 | >=4
Percentile | Number of records without de-energized circuits | Number of circuits involved without de-energized circuits
50th | 4,132 | 489 of 1,726
75th | 1,354 | 240 of 1,726
80th | 1,053 | 201 of 1,726

## Slide 5
PSPS days
Table using FBI => 4
PSPS Days – All Circuits in PSPS Days
www.technosylva.com
Copyright © 2021. Technosylva Inc., La Jolla, CA.
Table using FBI => 3
Percentile | Number of records without de-energized circuits | Number of circuits involved without de-energized circuits
50th | 4,132 | 489 of 1,726
75th | 1,354 | 240 of 1,726
80th | 1,053 | 201 of 1,726
Percentile | Number of records without de-energized circuits | Number of circuits involved without de-energized circuits
50th | 9,597 | 773 of 1,726
75th | 2,185 | 345 of 1,726
80th | 1,640 | 281 of 1,726

## Slide 6
Non-PSPS days
Non-PSPS days – all circuits in PSPS days
www.technosylva.com
Copyright © 2021. Technosylva Inc., La Jolla, CA.
We extracted all circuit records for non-PSPS days (n = 134,392)
  Each circuit has fire risk metrics every 3 hours
  We randomly selected non-PSPS days during the fire season (May-Dec)
  We filtered data using the thresholds previously calculated
    (Buildings OR Fatalities) and FBI (for each percentile threshold)
    Circuits that met the threshold criteria
Percentile | Buildings | Fatalities | FBI
50th | 182 | 0.22 | >=4
75th | 455 | 0.51 | >=4
80th | 535 | 0.57 | >=4
Percentile | Number of records | Number of circuits involved
50th | 605 (0.45%) | 94 of 1,650
75th | 118 (0.087%) | 24 of 1,650
80th | 90 (0.067%) | 20 of 1,650

## Slide 7
Non-PSPS days
Non-PSPS days vs PSPS days
www.technosylva.com
Copyright © 2021. Technosylva Inc., La Jolla, CA.
PSPS days
Percentile | Number of records | Number of circuits involved
50th | 0.45 % | 5.6 %
75th | 0.09 % | 1.5 %
80th | 0.07 % | 1.2 %
Non-PSPS days
Percentile | Number of records without de-energized circuits | Number of circuits involved without de-energized circuits
50th | 1.9 % | 28.3 %
75th | 0.6 % | 13.9 %
80th | 0.5 % | 11.6 %
In p75 and p80 the number of circuits and records that met the threshold criteria were 10 times higher during PSPS days compare to non-PSPS days

## Slide 8
PSPS days - SCENARIOS
PSPS days - SCENARIOS
www.technosylva.com
Copyright © 2021. Technosylva Inc., La Jolla, CA.
Thresholds: the 80th percentile values for consequence ((535 BI or 0.57 PF) and FBI =>4) and ERMcriteria (FPI >12; WS>31mi/h; WG>46mi/h)
Only circuits for PSPS event days that were not de-energized are included.
  Number of circuits during PSPS days that met the different criteria.
 | Consequence p80 | FPI | WS or WG | FPI or WS or WG | BI 50 or PF 0.9
Consequence p80 | 201 | 60 | 55 | 26 | -----
FPI |  | 472 | 161 |  | 117
WS or WG |  |  | 406 |  | 39
FPI or WS or WG |  |  |  |  | 26
BI 50 or PF 0.9 |  |  |  |  | 1,191